## Slide 1: Amit graduation project
Group Alex 41
Lab Management

## Slide 2: Lab Management
Ahmed Mohamed khairy
Ali Ramadan Ramadan

## Slide 3: Block diagram

## Slide 4
Microcontroller
LCD
MP3 (UART)
EEPROM (I2C)
RTC (I2C)
KEYPAD
MODE_SELECT (GPIO)

## Slide 5: Introduction

## Slide 6
It is important to use technology to facilitate organizing and managing lab visitors, there are some requirements to implement this project :
  Four Work days to choose from.
  Each day has 3 times to choose from.
  Each time has specific number of groups .
  Using keypad to select day and time and choose grade number and write group id.
  Using LCD to display these data.
  In case of power failure the time is continue without any problems when power restored.

## Slide 7: FLOW CHART

## Slide 8
START
Initiate drivers
  LCD
  MP3
  EEPROM
  RTC
  KEYPAD
Save first address for each day in an array
If(first run time)
  Save current date and time in RTC
Else
  Read current date and time from RTC
Check running mode
  Live
  Edit
Infinite loop
If(live mode)
    Read date and time from rtc
    Display on lcd
    If (8am)
      Erase past appointments from eeprom
      Update current day appointments
    Every period of minutes
      Say current group numbers
      Say warnings about tools and cleaning
    5 minutes before time ends
      Say warning about leaving lab
  Else(edit mode)
    Main page > instruction page > grade page
    Grade page
      Select student grade
      Next is group page
    Group page
      Write group id
      Next is day page
    Day page
      Select day
      Next is time page
    Time page
      Select time
      Next to submit page
    Submit page
      Get day, time from saved data
      Save data in specific location
      Save group number in the next address
      If success go to grade page
      Else go to time page to select another time

## Slide 9: components

## Slide 10
KEYPAD
  They are used to choose grade, day and time options
  Write group id
  Back to previous menu
LCD
  Display live date and time
  Display different menus to choose from
MP3 module
  Play group id
  Play some instructions in lab
RTC module
  Get live date and time
EEPROM module
  Used as database to save appointmnets